## Slide 1: Untangling ageing and age cohort effects in auto use and active transportation Mark Bradley

## Slide 2: What is the problem?
Most travel demand models assume that travel behavior in a given context (the model coefficients) will remain constant into the future >>>
According to most models, in 20-30 years, all else equal…
people in my generation will behave the same as people in my parents’ generation are behaving now.
people in my children’s generation will behave the same as people in my generation are behaving now.

## Slide 3: Source: https://www.visualcapitalist.com/us-population-pyramid-1980-2050/

## Slide 4: How are the generations different right now?
  OBJECTIVE / USUALLY OBSERVABLE IN DATA
Age
Gender
Household lifecycle
Work/school status
Income
Race/ethnicity
Vehicle availability
etc…
  SUBJECTIVE / RARELY OBSERVABLE IN DATA
  Past travel experiences
  Developed travel habits
  Attitudes and habits related to health, exercise
  Attitudes and behavior related to the environment
  Attitudes toward & use of new technologies
  Participation in the “shared economy”

## Slide 5: To separate the effects of ageing versus generational differences, we need consistent longitudinal data over a long period
  EXAMPLE: First presented at the “Zephyr Panel on Behavior Dynamics: The Future Accelerated” in December 2020
  Reason: An update of the IMPACTS 2050 model developed for NCHRP Report 750: Strategic Issues Facing Transportation. Volume 6: The Effects of Socio-Demographics on Future Travel Demand
  Method: A longitudinal analysis of the National Household Travel Survey (NHTS) from 1995, 2001, 2009 and 2017 for various types of travel choice models.
  Also controlled for income, race/ethnicity, household lifecycle, employment status, vehicle availability and residence area type, as well as year-specific effects

## Slide 6: Age group and Generation coefficients from an adult non-work trip mode choice model

## Slide 7: NEW for this presentation: an analysis of vehicle-miles traveled (VMT) by Adults over time
  Previous research: McDonald, N. (2015). " Are Millennials Really the “Go-Nowhere” Generation?" Journal of the American Planning Association. (Used 1995, 2001, 2007 NHTS.)
  RSG, Coogan, M., RAND Corp., Nelson/Nygaard. (2017). “NCHRP 08-36, Task 132. Understanding Changes in Youth Mobility”.
  Updated method: Added data from 2017 and 2022 NHTS. Extended the focus beyond Millennials to all adults.
  Again, controlled for income, race/ethnicity, household lifecycle, employment status, vehicle availability and residence area type, as well as year-specific effects

## Slide 8: NEW for this presentation: an analysis of vehicle-miles traveled (VMT) by Adults over time. What are the trends behind the aggregate numbers?
Chart: Average daily VMT per adult for work and non-work trips
| 1995 | 2001 | 2009 | 2017 | 2022
work trip vmt | 10.7389 | 10.581 | 7.3552 | 7.5509 | 6.7345
non-work trip vmt | 17.3454 | 18.7373 | 13.4296 | 14.1917 | 10.2366

## Slide 9: Modeling approach: Log-Linear regression at the person-day level
  Age group
  Age cohort
  Worker status
  Gender by presence
  and age of children
  Household size
  HH vehicle availability
  Log of HH income (2025 $)
  Race and ethnicity (not significant)
  The dependent variable is LN(vehicle-miles as a driver on the travel day + 1.0). The independent variables are:
  Log of Census block group population density
  Non-MSA area
  Day of the week
  Month of the year
  Proxy data bias
  Residual constant for each survey year (not very large)

## Slide 10: Generational effects in the opposite direction as for walk and bike in the previous example
Chart: Regression Coef. by Age Group
| age 18-24 | age 25-34 | age 35-44 | age 45-54 | age 55-64 | age 65-74 | age 75 up
 | 0.615 | 0.522 | 0.321 | 0 | -0.168 | -0.305 | -0.736
Chart: Regression Coefficients by Age Cohort
| Great | Silent 1 | Silent 2 | Boom 1 | Boom 2 | Gen X 1 | Gen X 2 | Millennial 1 | Millennial 2 | Gen Z
 | 0.888 | 0.824 | 0.746 | 0.625 | 0.436 | 0.247 | 0 | -0.26 | -0.506 | -0.854

## Slide 11: AGE EFFECTS mostly disappear when age cohort effects are removed- they are confounded
Chart: Regression Coef. by Age Group when Age Cohort Effects Included
| age 18-24 | age 25-34 | age 35-44 | age 45-54 | age 55-64 | age 65-74 | age 75 up
 | 0.615 | 0.522 | 0.321 | 0 | -0.168 | -0.305 | -0.736
Chart: Regression Coef. by Age Group w/ Age Cohort Effects Removed
| age 18-24 | age 25-34 | age 35-44 | age 45-54 | age 55-64 | age 65-74 | age 75 up
 | 0.003 | 0.169 | 0.259 | 0 | 0.188 | 0.224 | -0.066
The model fit also goes down very significantly..
R-squared 0.263 vs 0.247

## Slide 12: Longitudinal data can also indicate shifts in other effects – GENDER Differences becoming less important than household lifecycle, with shift mainly occurring between 2001 and 2009 surveys
Chart: Coefficients for gender and presence / age of children before and after 2009 survey
| male- no kids | male- kids age 0-5 | male- all kids age 6+ | female- no kids | female- kids age 0-5 | female- all kids age 6+
Before 2009 | 0 | 0.076 | 0.114 | -0.563 | -0.469 | -0.39
2009 and after | 0 | 0.115 | 0.126 | -0.345 | -0.15 | -0.115

## Slide 13: Conclusions
  Ageing effects are confounded with age cohort (generation) effects in cross-sectional data.
  Longitudinal data are needed to “untangle” the effects.
  Each generation appears to drive somewhat less and walk and bike somewhat more than the generation it replaces, all else equal.
  More frequent and consistent national travel surveys (like those in several other countries) would improve such analysis
  It is particularly important for longer-term forecasting models when shifts in the future age profile are expected. (This is the case for the models used for most regional transportation plans.)
  Assumptions needed for new adults (e.g. Gen Alpha the same as Gen Z)

## Slide 14: THANK YOU
Mark Bradley
MarkB@BlueDoorSR.com