## Slide 1: Preparing the Twin Cities Model for Pandemic-Related Uncertainty
Modeling Mobility Conference
September 14, 2025
Andrew Rohne

## Slide 2: Disclaimer
This work does not represent any policy or plan by the Metropolitan Council

## Slide 3: Development Timeline
2018: Household Survey
2020: Initial ActivitySim deployment, light calibration & validation
2018 data and base year
😷
2022: Household Survey
2024-2025: ActivitySim Updates, calibration, validation
2022 data, 2021 base year
2024: Household Survey

## Slide 4: Survey Comparisons
Surveys were loaded into a visualization tool for comparison
Expected – and saw – changes to WFH, telecommuting, daily activity pattern, some mode choice changes

## Slide 5: WFH and Telecommute Changes
Note: Survey data. Model was calibrated to ACS data
Notes: Survey comparisons!

## Slide 6: Daily Activity Pattern Changes

## Slide 7: What I Did
Added a covid factor in some models
  Allows a return-to-office test
  Factor – 1.0 for post-covid, 0.0 for pre-covid, anything in between is allowable
  Specifically: Work from home, telecommute frequency, daily activity pattern
Compared models
  Checked all models that shouldn’t change to ensure they didn’t
Caveats
  Synthetic population and SEDATA did not change
  Road and transit network did not change

## Slide 8: Easy Results

## Slide 9: Easy Results

## Slide 10: Trip Output Results
 | Total Trips
Pre-Covid | 14,235,404
Post-Covid | 13,146,988
 | Asim VMT
Pre-Covid | 95,441,790
Post-Covid | 83,577,873
7.6% Trip Decrease
12.4% VMT Decrease
 | Asim Transit
Pre-Covid | 156,989
Post-Covid | 115,434
26.5% Linked Ridership Decrease
Notes: Per MNDOT, the annual VMT per person fell by 7.3%, the model may be overreacting
Per Met Council Transit Data, transit fell by 52%

## Slide 11: Conclusions
Periodic surveys can capture trends in travel
Model can react as designed; use caution in unadjusted steps
Such a study brings up lots of questions…
  Should the synthetic population remain static?
  Should we push to include occupation in synthetic populations?
Should supply (especially transit) remain static?