## Slide 1: Speaking the Same Language: Cross-walking Truck Classification Systems for Efficient Freight Modeling
GVWR
8.5-10k lbs.
Long-haul
Kaveh Shabani
Fatemeh Ranaiefar

## Slide 2: Background
Various vehicle classifications
Crosswalks needed!
axle-based
weight-based
Various classes based on GVWR

## Slide 3: Data Sources
National VIUS (Vehicle Inventory and Use Survey), 2002 (and 2021)
  National survey of truck drivers
  Surveyed about 100k (150k in 2021) truck drivers
  Currently used in freight models for payloads and percent empties
  All truck weights (no empty weights in 2021 data)
  Activity type in 2021 data (some commercial activity vs. personal use only)
    ~ 57% of data records: “some or all commercial activity” (~17% of total vehicles)
    ~ 14% of data records: “vehicle not in use” or “not reported” (~8% of total vehicles)
  Less detail on number of axles in 2021 data
California VIUS, 2017
  Only trucks serving California
  Truck weights > 10k lbs.
  More than 50% of surveyed trucks > 33k lbs.
  Sample size: 14.7k (CA), expanded: 759k (CA)
National FHWA Study, 2021
  Uses vehicle registration data from 2019
  More details on FHWA Classes 3 and 5
  Sample Size: 1.3 M (U.S.), expanded: 175 M (class 2 and above)

## Slide 4: FHWA-13 Class Compositions (2002 National VIUS)
Chart: FHWA 13-Class
| 3 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
Class 1 – 0 to 6,000 lbs. | 0.6185 | 0.036003 | 0.0014173 | 0.00031377 | 0.030655 | 0 | 0.001545 | 0 | 0 | 0
Class 2a – 6,001 to 8,500 lbs. | 0.16659 | 0.070115 | 0.0012401 | 0.00031377 | 0.044397 | 0 | 0.00038625 | 0 | 0 | 0
Class 2b – 8,501 to 10,000 lbs. | 0.053665 | 0.10173 | 0.0023031 | 0 | 0.039746 | 0 | 0.0027037 | 0 | 0 | 0
Class 3 – 10,001 to 14,000 lbs. | 0.049789 | 0.18649 | 0.0061121 | 0.00062755 | 0.067442 | 0.00017305 | 0.0027037 | 0 | 0 | 0
Class 4 – 14,001 to 16,000 lbs. | 0.019858 | 0.093688 | 0.0033661 | 0.00031377 | 0.035518 | 0 | 0.001545 | 0 | 0 | 0
Class 5 – 16,001 to 19,500 lbs. | 0.018015 | 0.085723 | 0.0063779 | 0.00094132 | 0.028753 | 0.00011537 | 0.00309 | 0 | 0 | 0
Class 6 – 19,501 to 26,000 lbs. | 0.043402 | 0.22909 | 0.027106 | 0.0053342 | 0.10063 | 0.0031149 | 0.022402 | 0 | 0 | 0
Class 7 – 26,001 to 33,000 lbs. | 0.016776 | 0.1208 | 0.044911 | 0.006903 | 0.094292 | 0.0077873 | 0.01545 | 0.0058997 | 0 | 0
Class 8 – > 33,001 lbs. | 0.013408 | 0.076351 | 0.90717 | 0.98525 | 0.55856 | 0.98881 | 0.95017 | 0.9941 | 1 | 1
Chart: FHWA-13 classes and SCAG HDT truck Classes
| L (class 3) | M (class 5-7) | H (class 8+)
light-heavy (8,500 to 14,000 lbs.) | 0.48137 | 0.10284 | 0.019039
medium- heavy (14,00I to 33,000 lbs.) | 0.45624 | 0.21607 | 0.05379
heavy-heavy (>33,000 lbs.) | 0.062389 | 0.68109 | 0.92717

## Slide 5: SCAG HDT Truck Classes (National VIUS vs. California VIUS)
Vehicles with different weight characteristics can have similar number of axles. For example, this can be seen when larger pickups pull utility trailers. (The FHWA would still classify it as a Class 3 vehicle.)
Chart: National VIUS (2002)
| light-heavy (8.5-14k lbs.) | medium- heavy (14-33k lbs.) | heavy-heavy (>33k lbs.)
L (class 3) | 0.31 | 0.17 | 0.01
M (class 5-7) | 0.64 | 0.75 | 0.39
H (class 8+) | 0.05 | 0.08 | 0.6
Chart: California VIUS (2017)
| light-heavy (8.5-14k lbs.) | medium- heavy (14-33k lbs.) | heavy-heavy (>33k lbs.)
L (class 3) | 0.34 | 0.2 | 0
M (class 5-7) | 0.66 | 0.77 | 0.15
H (class 8+) | 0.01 | 0.02 | 0.85

## Slide 6: Approach for FHWA Class 3 (2 axle-4 tire)
  National VIUS (2002) - CA
  FHWA Study (2019 private registration Data for all vehicles in the U.S.)
  Estimated All Commercial Vehicles in FHWA Class 3
  Estimated Commercial Vehicles in FHWA Class 3
  With 8.5-14k lbs. GVW
  *FHWA study (2020)
  Uses vehicle registration data from 2019 for all U.S.
  Four private vehicle registration data sets acquired by the FHWA
  Uses a methodology to assign FHWA-13 vehicle classification to observations in the mixed-duty and heavy-duty vehicles data
  Distinguishes between two-axle, four-tire and two-axle, six-tire vehicles (i.e., FHWA-13 class 3 and 5)
  The approach uses proxy variables such as GVWR, Fuel Type, Number of Cylinders, Engine Displacement, etc.
  Sample size: 1.3 million, expanded: 175 million (class 3 and above)
  Details of data expansion not disclosed!
  Move some of class 5 to LHDT in a later update!
  Expanded National VIUS (2002) – FHWA Class 3 trucks (only commercial vehicles)
All Class 3 trucks in National VIUS = 78,065,379
Notes: *linking FHWA and NHTSA Vehicle's Type , Cambridge Systematics for FHWA – the report is under review by FHWA

## Slide 7: Crosswalk for SCAG
FHWA/SCAG | LH | MH | HH
3 | 82% | 18% | 0%
5 | 35% | 64% | 1%
6 | 5% | 25% | 70%
7 | 5% | 5% | 90%
8 | 25% | 5% | 65%
9 | 0% | 3% | 97%
10 | 0% | 3% | 97%
11 | 0% | 5% | 95%
12 | 0% | 0% | 100%
13 | 0% | 0% | 100%
FHWA 13-class to SCAG truck class Conversion (updated)
  ~80% of FHWA Class 3 are commercial vehicles
  ~3% of FHWA Class 3 are included in the HDT model
  ~2.6% to LH, 0.4% to MH
The composition of trucks vary spatially and temporally. So, a fixed mapping factor is needed but not adequate.
Trip rates, Trip distribution, Mode cost, Port trips, Intermodal trips, TOD factors, Trip assignment, Model validation

## Slide 8: Contact
Kaveh Shabani
kshabani@camsys.com
C: 971-344-4323

## Slide 9: Appendix

## Slide 10: FHWA Truck Classification

## Slide 11: FHWA Truck Classification

## Slide 12: FHWA Class 5
Source: txdot.gov