## Slide 1: Improving the Modeling of Truck and CVs
Using GPS Truck Big Data in NYMTC’s Truck Model
2025 Modeling Mobility Conference
Brent Selby, John Gliebe (speaker)
September 17, 2025

## Slide 2: Truck Model Objectives
Truck trips
  Light trucks/commercial vehicles
  Medium trucks
  Heavy trucks
Commercial trips only
  Freight
  Non-freight
Passenger trips modeled in the ABM
Region – NYMTC
  NY-NJ-CT
  Large, complex
Trip types
  Internal (I-I)
  Internal-External (I-E)
  External-Internal (E-I)
  External-External (E-E)
Notes: Overall description of the model
Give background for what we are talking about and what the model does.
This can be short as people at MoMo are probably fairly aware of what truck models are.

## Slide 3: Model Structure
Long Distance Model
  IE/EI, EE trips
  Previously included all >50 mi
  FAF based
Short Distance Model
  I-I trips
  3 step model
  Now LOCUS Truck based
Maintained submodels in update
FAF Flows
Disaggregation
Payload Factors
Empties and Balancing
IE/IE/EE Trip Table
Trip Generation
Sub-Model
Trip Distribution
Sub-Model
II
Trip Table
Assignment
Notes: More background
Important to know, but not that hard hitting.

## Slide 4: Previous Model
FAF data used for all trips above 50 miles
  Best data available
  Aggregate FAF zones
Short distance based on surveys
  Trips rates and avg distances from other times/places
  Gravity model for distribution
  Limited underlying data
Notes: We want them to understand how it was done in the past and why.
This sets up the next slide and how/why we can improve it.
At the time this was created FAF was the available data (so it was stretched to be applied as much as possible)
Subtext: the data they had on short distance trips was minimal and came from other places years before. There was a patchwork of assumptions and estimates.

## Slide 5: Updated Short Distance Model with LOCUS
GPS-based LOCUS Trucks
  Local and comprehensive
  Recent - 2023 data
  Actual, expanded truck trips
  Much more disaggregate
New short distance model
  All internal trips
  Estimated with LOCUS Trucks
  Destination choice replaced trip distribution
  Segments
    Vehicle weight
    Time of day
    Truck behavioral pattern
Notes: Behold: data. Better input data means better model output.
We can now produce a model based on real truck trips that happened in the region.
The data set is huge and disaggregate – we used the TAZs.
(map shows trip generation by TAZ)

## Slide 6: Model Estimation
Trip generation
  Estimated by TAZ
  Driven by employment
  Included accessibility indices (AI)
Destination Choice
  Results varied by vocation, time
  Used travel time, employment, AI
Both segmented fully
  Possible with large data size
Vocation Name | Behavior
Door-to-Door | Frequent, Short Stops
Hub and Spoke | Multiple round trips with base location
Local | Limited geographic range of activity
Regional | Wider range, but returns to location
Long-Distance | Wide range, does not frequently return
Notes: We used the LOCUS OD table to get trip generation by TAZ and then estimated the model.
Trip gen model used employment and acc indices
Destination choice also used the LOCUS OD table with travel time, employment, and acc indices as variables.
(if asked, tolls were tested but not significant. Commercial travel may react to tolls in routing, but not really in destination choice)
We estimated coefficients for each segment – vocation and time of day – for each submodel. This is not possible with a small dataset.
Using the segments the model could better capture the distribution patterns of trucks, especially their trip length distributions.

## Slide 7: Conclusions
Big Data has changed the game for truck modeling in development and estimation
Better inputs make better models
  Precision/accuracy
  Timeliness (recent data)
  Locality
  Sample size
  Expansion
Notes: Reiterating – we have precise, accurate, recent, carefully expanded data from real truck trips in the NY region
If you do not like this slide you can change it or even drop it

## Slide 8
Thank You for Your Time
Please reach out with additional questions or queries.
Brent Selby
bselby@camsys.com
John Gliebe
jgliebe@camsys.com